| General-purpose Resistors/Carbon Film Resistors |  |
| --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF General purpose CF Carbon film 0.25, 0.5 2.2 5.1M 2, 5 CFP Carbon film (Flame retardant) 0.25, 0.5 2.2 1M 2, 5

|  | Precision Resistors/Metal Film Resistors |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF Precision MF Metal film (Precision, Low T.C.R.) 0.25, 0.5 0.51 5.11M 0.5, 1, 2 SN Metal film (Precision, Low T.C.R.) 1, 2 4.99 1.5M 0.5, 1, 2 MFP Metal film (Flame retardant) 0.25, 0.5 10 100k 1 SNF Metal film (Flame retardant) 0.25, 0.5 0.47 100 5 MRS Metal film (Radial) 0.125 0.3 10 - 1M 0.01, 0.02, 0.05, 0.1, 0.25, 0.5 LF Metal film (L-shape lead) 0.125 0.5 1 1M 0.5, 1, 2,5 LFF Metal film (Flame retardant, L-shape lead) 0.25 1 100k 1, 2 RNS Metal film (Precision, Low T.C.R.) 0.125 1 0.2 6.8M 0.1,0.25,0.5,1 SF Metal film (Molded, High precision) 0.125 0.5 100 5.11M 0.01, 0.02, 0.05, 0.1, 0.25, 0.5

|  | Resistors for High Voltage Circuit |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF High voltage RK Metal glaze film 0.25 1 100k 100M 1, 2, 5 RK1/2G Discharge path resistor (UL1676) 0.5 1M 12M 5 RK26 Metal glaze film (L - shape lead) 0.25 100k 33M 1, 2, 5 RCR Anti surge resistors (UL1676)/(EN60065) 0.25 3 3.3 100M 1, 5 GS High voltage, High power 0.25 12 500k 10G 0.5, 1, 2, 5, 10 RK92 High voltage (Metal glaze film) 0.5 1.1 1M 1G 1, 2, 5, 10, 20 PCF Anti surge・pulse ceramic resistor 0.5 2 3.3 390k 10, 20 HPC Anti surge・pulse ceramic resistor 0.5 5 3.3 390k 10, 20 CPCN Ceramic resistor 0.5 2 1k 15k 20 P High voltage 1.5 250 10 6G 5, 10, 20

|  | Power Type Resistors |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF Power MOS Metal oxide film (Small size) 0.5 5 10 100k 1, 2, 5 MOSX Metal film (Small size) 0.5 5 0.1 9.1 1, 2, 5 MO Metal oxide film 0.5 3 10 150k 2, 5 MOX Metal film 0.5 3 0.2 9.1 2, 5 SPR Special power resistor 0.25 5 2.2 1M 1, 2, 5 SPRX Metal film (Small size) 0.25 5 0.1 2 5 BGR Cement case (Wire wound, Glass core) 5 40 0.39 390 5, 10 BWR Cement case (Wire wound, Ceramic core) 1 20 0.1 390 1, 2, 5 BSR Cement case (Metal oxide film) 2 20 430 75k 5

|  | Wirewound Resistors |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF Wire wound CW Wire wound 0.25 5 0.01 390 0.25, 0.5, 1, 2, 5, 10 CW-H Wire wound 1 3 0.1 3k 0.5, 1 RW Wire wound (Precision, Low T.C.R.) 0.5 10 0.1 62k 0.5, 1, 3, 5

|  | Current Sense Resistors/Low Resistance Resistors |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF Low resistance BPR Cement case (Metal plate) 2 10, 5+5, 7+7 0.01 1 5, 10 LR Metal wire — 3m 100m 3, 5

|  | Resistor Networks/Resistor Array |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF Network MRP Thin film R network (Balance resistors) 100m 50 100k 0.1, 0.25, 0.5, 1 RKL Thick film R network (Low profile) 125m, 200m 22 1M 1, 2, 5 RKC Thick film R network (Standard) 20m 250m 22 2.2M 1, 2, 5 RKH Thick film R network (Power type) 250m, 500m 56 2.2M 1, 2, 5

|  | Linear P.T.C. Resistors/Thermal sensers |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF Linear LT Linear PTC 0.16, 0.25 10 51k 2, 5 LP Linear PTC (Precision) 0.063, 0.125 1 100k 1, 2, 5

|  | Platinum Thin Film Thermal Sensors |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF Platinum thin film thermal sensors SDT101 Platinum thin film ,thermal sensors 0.125 10, 100, 500 0.5, 1 SDT310 Platinum thin film ,thermal sensors (L-shape lead) — 10,100, 500, 1k 0.059, 0.12, 0.39,10

|  | Fusing Resistors |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF Fusible RF Fusing resistor 0.17 2 0.1 15k 5 RF26 Fusing resistor (L-shaped lead) 0.25 0.1 1k 5 RF25CC Fusing resistor (Constant current fusing type) 0.25 0.1 0.91 10 WF Thermal fuse built-in resistor 1.2 3.5 1 10k 5, 10

|  | Jumper Wires |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF Jumper Z Jumper (Coating type) — 20m max. — J-Z Jumper (Molded) — 10m max. — JL Jumper wire (Taping) — — —

|  | CR Networks |  |
| --- | --- | --- |

Category Type Features Power Rating (W) Resistance Range(Ohm) Tolerance (%) PDF CR CR Thick film C/R network (Customorders) — 10 1M 5

Common Specification Items PDF Minimum Ordered Quantity Recommended Pad Dimensions Packagings For Chip Components Axial Tapings Radial Taping Forming Color code•Resistance marking•E series numbers